## Slide 1: A wearable motor imagery BCI with online feedback
Eng. Antonio Esposito
Ph.D. student in metrology at politecnico di torino

## Slide 2: objective and strategy
Being capable to perform motor imagery
  rehabilitation
  control
Motor imagery can be improved with an online feedback
Compare different feedbacks
  visual feedback
  haptic feedback
  multimodal feedback

## Slide 3: Wearable BCI system
EEG acquisition with three bipolar channels with FlexEEG (wet electrodes)
trial indications and visual feedback
vibrotactile feedback on torso
with haptic suit by bHaptics
Notes: Wearability is a key novelty

## Slide 4: EEG online processing
125 Sa/s sampling rate
feedback direction and intensity
protocol timing
UDP
4-8 Hz
6-10 Hz
8-12 Hz
36-40 Hz
…
filter bank
CSP
MIBIF
F1
F2
F3
F4
…
Fn
class
info
motor imagery class and score
naïve bayesian
classifier
EEG

## Slide 5: neurofeedback protocol
EEG acquisition without feedback
3 x 30 trials
model trained on block MI EEG data
control of feedback intensity
biased feedback (always correct direction)
BLOCK MI
BLOCK NF
visual: 3 x 30 trials
haptic: 3 x 30 trials
multimodal: 3 x 30 trials

## Slide 6: Preliminary results
  Moderately trained subject
  First session (2 h)
  Feedback order was
    visual
    multimodal
    haptic
  Visual feedback appears the best, yet it is the more intuitive one
Notes: Feedback is always better than no feedback

## Slide 7
questions?